Formulation of the microscale transport problem non-dimensionally

where Pe = Microscale Peclet no. = Rv/Dmol

Boundary Conditions

At z* = 0,    c* = 1

At z* = k,

At r* = 0,

At r* = 1,

where s* = mass of adsorbed solute per unit area

r* = 1

z* = 0										    z* = k

r* = 0

Considering equilibrium adsorption at the capillary wall, we get

as s* = (c *

( = rate constant = kd/r

Therefore, at r* = 1,

Initial Condition

c * = 0 in the capillary tube

In order to solve the above equation in FlexPDE, I formulate it in the following way:

EQUATIONS     { PDE's, one for each variable }

C:	(dzz(C)+(1/r)*dr(r*(dr(C))))=Peclet*(dt(C)+(1-r^2)*dz(C))

Ds:	dt(C)=Ds

BOUNDARIES    { The domain definition }

REGION 1 'TUBE'    { For each material region }

START(z1,r1)  { Walk the domain boundary }

value(C)=1

{natural(C) = Peclet*(1-r^2)*(1-C)}

{MESH_SPACING = if (r<0.7) then 0.2 else 0.01}

line to (z1,r2)

natural(C)=-kappa*Peclet*Ds

{}

{MESH_SPACING = if (z<1) then 0.1 else if (z<25) then 0.2 else 0.1}

line to (z2,r2)

natural(C)=0

line  to (z2,r1)

natural(C)=0

line to finish

My Problems

A] If I provide the equation in FlexPDE keeping the dc/dt term on the LHS i.e.

Peclet*(dt(C)+(1-r^2)*dz(C))= (dzz(C)+(1/r)*dr(r*(dr(C))))

I fail to get a solution!!

B] If I put the Peclet no. on the LHS i.e.

(1/Peclet)*(dzz(C)+(1/r)*dr(r*(dr(C))))= dt(C)+(1-r^2)*dz(C))

although the equation is still the same, I get a different solution!!!

C]  The solution takes an infinitely long time convergence keeping the default errorlimit = 0.001…Why!!

I believe that the problem is lying somewhere in the way I am formulating it in FlexPDE….I wish to seek advice.